## Slide 2
10.10.2023
M. Samet Yakut
Advanced Design and Optimization in Hydro Generators

## Slide 3: Outline
Interactive Link Between MATLAB/ANSYS
Optimization Algorithm
  Variables
  Constraints
  Objective Functions
  Penalty Function
Results
Future Plans

## Slide 4: Interactive Link Between MATLAB/ANSYS
No direct connection between MATLAB and ANSYS
  VBS is used as medium
MATLAB runs main algorithm
  Variations are written in VBS
VBS runs ANSYS
  Simulation results are obtained
Postprocessing is conducted in MATLAB
Variables, Constraints
Variation
Simulation
Results

## Slide 5: Optimization Algorithm
Genetic algorithm
Pros
  Used when derivative is not available
  Provides good enough solutions fast enough
  Can be multi-objective
  Applicable in both continuous and discrete problems

## Slide 6: Optimization Algorithm
Genetic algorithm cons
  Can be computationally expensive depending on objective function
  Does not guarantee the optimality of the solution
  If not tuned properly, GA does not converge
Parameters tuned with trial-error methodology [1]
[1] https://www.sciencedirect.com/science/article/pii/S2210650211000022

## Slide 7: NSGA – II
Non-dominated Sorting Genetic Algorithm – II is used
  A multi-objective, GA based algorithm
  Uses elitist principle
  Uses explicit diversity preserving mechanism (Crowding Distance)
  Emphasizes the non-dominated solutions
Dominance: if in at least one objective, is dominating
[1] https://oklahomaanalytics.com/data-science-techniques/nsga-ii-explained/

## Slide 8: NSGA – II: Variables
: Ratio of inner diameter to outer diameter
: minimum airgap in mm
: axial length in mm
: slot width in mm
: slot height in mm

## Slide 9: NSGA – II: Constraints
Slots must fit in the stator core, i.e., outer diameter should be greater than sum of inner diameter and slot height
Rotor poles must fit in the airgap perimeter

## Slide 10: NSGA – II: Objective Functions
Problem – I: Refurbishment of hydro-generator by alternating winding type
Constraints – I: Constant outer diameter, same rotor geometry
Problem – II: Design of a hydro-generator with Roebel bars
Constraints – II: Constant (but different from 1st problem) outer diameter, same rotor geometry
Problem – III: Design of a hydro-generator with Roebel bars
Constraints – III: Constant outer diameter (same as 2nd problem), integer slot

## Slide 11: NSGA – II: Objective Functions
Objective functions are
  Initial cost
  Efficiency
  Subject to

## Slide 12: NSGA – II: Penalty Function
SCR should not be less than 0.8
Penalty function is added to the cost function if penalty constraints are satisfied
Hence
  where A is a very large number compared to initial cost

## Slide 13: Results: Do = 6858 mm
150 Population (completed in 13h)

## Slide 14: Results: Do = 6858 mm
300 Population (completed in 53h)

## Slide 15: Results: Do = 8000 mm
300 Population (completed in 53h)

## Slide 16: Past Plans
Completing winding design (as well as its alternatives)
Eccentricity analyses
Creating basis for advanced design and optimization
Future Plans
Completing optimization studies
Creating manufacturing documents
Manufacturing mock generator