## Slide 2
ALTERNATING WINDING TYPE OF 44 MVA HYDRO GENERATOR
M. Samet YAKUT
Advisor: Ozan Keysan
November 23, 2023
EE590 Seminar, METU EE Dep.

## Slide 3
Largest low-carbon electricity generation technology is hydropower [1]
IEA, Low-carbon electricity generation by technology, 2020, IEA, Paris https://www.iea.org/data-and-statistics/charts/low-carbon-electricity-generation-by-technology-2020, IEA. Licence: CC BY 4.0
TWh

## Slide 4: Outline
Introduction
  Basic Terms & Definitions
Refurbishment Process
  Optimization
  Design of Roebel Bars
Conclusion

## Slide 5: Introduction
Salient pole synchronous machines
High voltage stator
Tens of kVA to hundreds of MVA

## Slide 6: Refurbishment
Installed capacity older than 30 years: 6205 MWs
  which accounts for 31.9% of large hydro generators [1]
Most old generators are over – designed
  cheapest way of increasing installed power
N. Tosun, G. Gülletutan, M. S. Yakut, D. Alp Yilmaz, Ö. Bayer and O. Keysan, "Winding Type Alternation of a Refurbished Old Generator," 2023 IEEE Workshop on Electrical Machines Design, Control and Diagnosis (WEMDCD), Newcastle upon Tyne, United Kingdom, 2023, pp. 1-6, doi: 10.1109/WEMDCD55819.2023.10110941.

## Slide 7: Winding Types
Lap Winding Wave Winding
M.M. Znidarich (2008) Hydro Generator High Voltage Stator Windings: Part 1 – Essential Characteristics and Degradation Mechanisms, Australian Journal of Electrical and Electronics Engineering, 5:1, 1-17, DOI: 10.1080/1448837X.2008.11464196

## Slide 8: Winding Types
Wave Winding |  | Lap Winding | 
Advantage | Disadvantage | Advantage | Disadvantage
Less outage duration | Complicated design | Simple winding schematic design | Complicated end connections
Simple end connection | Generally requires more coil types | Less type of coils | More outage time
Low number of external connection | Longer average winding pitches, therefore longer end windings | Allows bypass | Sophisticated production

## Slide 9: Problem Definition
Refurbishment of an old 44 MVA hydro generator by changing winding type from lap to wave
Constraints
  Constant outer diameter
  Same rotor geometry
Challenge
  Increasing efficiency

## Slide 10: Optimization: Variables
: Ratio of inner diameter to outer diameter
: minimum airgap in mm
: axial length in mm
: slot width in mm
: slot height in mm
: slot number

## Slide 11: Optimization: Constraints
Slots must fit in the stator core, i.e., outer diameter should be greater than sum of inner diameter and slot height
Rotor poles must fit in the airgap perimeter

## Slide 12: Optimization: Objective Function
Objective functions are
  Initial cost
Efficiency
Subject to

## Slide 13: Optimization: Penalty Function
SCR should not be less than 0.8
Hence
  where A is a very large number compared to initial cost

## Slide 14: Optimization: Results

## Slide 15: Design Methodology
Old Generator | Final Design
240 Slots | 300 Slots
Lap Winding | Wave Winding
Same rotor geometry, air gap, and outer diameter | 

## Slide 16: Roebel Bars
Single turn coils
Composed of multiple strands to reduce AC losses
Transposition is applied to minimize circulating currents

## Slide 17: Design of Roebel Bars
Different induced voltages in each strand
Circulating currents
Eddy losses

## Slide 18: Design of Roebel Bars
Selection of strand number
Selection of transposition angle
Limitations:
  Axial length
  Material strength

## Slide 19: Design of Roebel Bars

## Slide 20: Design of Roebel Bars

## Slide 21: Conclusion & Future Work
Refurbishment is important for sustanability
  Cheapest way of increasing installed power
Roebel bars are used to cancel circulating currents
  As well as reduce AC losses
Future Work: Optimization with different rotor geometries